Simulations of Vocal Fold Dynamics using MPMICE
Comer Duncan1
Department of Physics and Astronomy
Bowling Green State U., Bowling Green OH
Ronald Scherer1
Department of Communication Disorders
Bowling Green State U., Bowling Green OH
Jim Guilkey2 and Todd Harman2
Department of Mechanical Engineering
University of Utah
1 Work Supported by NIH
2 Work Supported by DOE

---
Outline
Basics of the structure of the larynx and the mechanism for the production of sound
Brief outline of MPMICE in relation to the vocal fold and aerodynamics problem
Preliminary vocal fold material model
Example simulations for Psubglottal=Patm+ 800 Pa
Current developments

---
How does phonation occur?

---
Phonation
Occurs in the the larynx at the level of the vocal folds

---
Phonation
Occurs in the vocal folds in the larynx
A stream of air with sufficient transglottal pressure induces the vocal folds to vibrate ~130 Hz for males & ~260 Hz for females

---
Phonation
Occurs in the vocal folds in the larynx
A stream of air with sufficient transglottal pressure induces the vocal folds to vibrate ~130 Hz for males & ~260 Hz for females
Sound shaped by pharynx, nasal & oral cavities

---
Basic overview of vocal fold dynamics
Lungs supply pressure of 1500 Pa above atmospheric pressure
Air flows through glottis inducing vocal folds to separate via positive pressure
Vocal fold material properties react to bring vf back toward initial state
Result is a 'pulse' of air which flows toward mouth

---
A Complete Vibration Cycle
Coronal slice across vf
VF begin closed(1)
Pressure gradient induces lower part to open first (2-4)
VF material reacts back to closure (5-8)
Note phased opening and closing
bold size 16{%DELTA P ~ simeq ~ 800 Pa}

---
Vocal Fold-Aerodynamics Modeling
Air flow exerts force on the vocal folds (vf) which are displaced
Material properties of vocal folds act back to restore the vf to their initial positions
Both the air flow and the vf material dynamics are interdependent
The physiological response is emergent
The problem is thus a type of Fluid-Structure Interaction problem

---
Multifield Approach to FSI
Averaged model which allows both air and vf to exist at any point of space with some probability--developed by Bucky Kashiwa et al at LANL, uses MPM for material modeling -developed by Sulsky et al and ICE for air
Strong interactions between the air and the vf materials (so N=2 here)
Full Navier-Stokes for air and transient nonlinear response of the vocal fold material
State vector for r-material
size 24 { langle M_r,bold u_r,e_r,T_r,v_r,%theta_r,bold %sigma_r,p rangle }

---
State of each material
Mr mass of r-material
ur velocity of r-material
er internal energy per unit mass of r-material
Tr temperature of r-material
vr volume per unit mass of r-material
volume fraction of r-material
Stress of r-material
P equilibrium pressure
size 32 %theta_r
size 32 bold %sigma_r

---
Basic Equations of Multifield Model of FSI
size 24 { {1 over V} {D_{r} M_{r}} over Dt ~~~~~~=" " 0}
Conservation of Mass
size 24 {1 over V {D_{r}(M_{r}u_{r})} over Dt ~=~ %theta_{r} nabla cdot bold %sigma + nabla cdot %theta_{r}(bold %sigma_{r} - bold %sigma) + sum from{s=1} to{N} bold f_{rs} }
Conservation of
Momentum
where
size 24 {bold %sigma ~=~ -p bold I}
mean stress
and
size 24 {bold f_{rs} ~=~ K_{rs} %theta_{r} %theta_{s} (bold u_r - bold u_s)}
momentum exchange force
size 24 { sum from{s=1} to{N} %theta_r = 1 " " drarrow " "0 = 1 - sum from{s=1} to{N} %rho_r v_r}
Solved to obtain equilibrium pressure

---
Basic Equations of Multifield Model of FSI
(cont'd)
size 24 {{1 over V}{D_{r}(M_{r}e_{r})} over {Dt} ~=~ - %rho_{r} p {D_{r}v_{r}} over Dt + %theta_{r} bold %tau_{r} : nabla bold u_{r} - nabla cdot bold j_{r} " "+" " sum from{s=1} to {N} q_{rs}}
Conservation of
Energy
where
size 24{ bold j_r ~=~ -%rho_r b_r nabla T_r}
Heat flux current
and
size 24{q_{rs} ~=~ H_{rs} %theta_r %theta_s (T_r - T_s)}
Internal energy exchange rate
size 24 bold %tau_r
is the deviatoric part of stress
and
size 24{{1 over V} {D_r(M_r v_r)} over {Dt} ~=~ f^{ ~%theta}_{r} nabla cdot bold u + %theta_r %beta_r {D_r T_r} over {Dt} - f^{~%theta}_{r} sum from{s=1} to {N} %theta_s %beta_s {D_s T_s} over {Dt}}
Evolution of
Specific Volume
size 24{{bold u } = sum from{s=1} to{N} %theta_s bold u_s}
size 28 f^{~%theta}_r " " =" " {size 20 %theta_r size 20 %kappa_r} over size 20{sum from{s=1} to {N} %theta_s %kappa_s}
mean velocity
and
where

---
A simplified one-material model showing geometry of vocal folds
A simplified one-material model showing geometry of vocal folds
A simplified coronal slice
Left and right vf are made of same material
Particles are used to characterize the vocal fold material

---
Material model
Particles with spatially varying material properties
Current simulations use Neo-Hook
Initial particle distribution taken from standard coronal slice of mid-plane vocal fold
Allows flexibility in material properties specification to more readily match histology

---
Sketch of Coronal Slice ala Hirano
Sketch of Coronal Slice
A step in the modeling is to abstract some simplified structures
Complete generality given up so that a computer model can be realistically devised.

---
Three Layer Model: relation to histology
Three Layer Model: relation to histology
Outermost layer = Mucosa: consists of the epithelium and the superficial layer of the lamina propria
Middle layer = Ligament: consists of the intermediate and deep layers of the lamina propria
Innermost layer = Deep layer: consists of the thyroarytenoid (vocalis) muscle

---
Example three-layer model
2D (z thickness small), each layer neo-hook
mucosa, ligament, & muscle
Variable shear modulus for each layer
Same constant bulk modulus for all layers K=289 kPa
Gmucosa =10 kPa; Gligament=30 kPa; Gmuscle=3.5 kPa

---
Example Simulations
ICE:
    - Advection: 2nd order
    - Pressure solve: implicit
    - BC at inlet: Dirichlet pressure, Neumann for velocity, temp, and density
    - BC at outlet: LODI for pressure, velocity, temp, density
    - Resolution: 87 x 320
MPM:
    - time integration: explicit
    - interpolator: GIMP
    - do grid reset: true
    - Neo-hook with modification to map color to shear modulus in initial data set, constant bulk modulus
    - Total particles: 11989

---
Movies
1. Close-up of the vocal folds with a graph of both the pressure and the opening width between the vocal folds as a function of time
distribution of materials in distinct layers
2. movie showing the whole computational domain with vf and aerodynamics
distribution of materials continuously varying

---
Current Developments
Current Developments
Use nonlinear material models, since experiments show that materials are not neo-Hookean--materials are hyperelastic transverse isotropic
Improve outflow boundary condition treatment
Extract pressure signal at outflow
Move to 3D !

---
Thanks !